## Slide 1
CLAWE INTERACTIVE EMITTERS APP
Data Schema
ClaweRadarInstance / ClaweRadarModeInstance / ClaweWaveformInstance — proposed protobuf + SQLite schema
v1.1 · Draft · 13 August 2026

## Slide 2
APPROACH
Two-Layer Storage — Matches PRISM.Database's Emitter Schema
▸ Canonical layer: the full radar (every mode, waveform, constraint, modifier parameter) is stored as one serialized protobuf blob per radar — the single source of truth, always read/written as a whole.
▸ Index layer: a few thin, flat SQLite rows (radar / mode / waveform — id, name, type only) exist purely so the UI can list and pick without deserializing a blob per row.
▸ Not a dead end: the blob stays canonical either way, so rollup tables can be added additively later — a schema-update step walks existing blobs into new tables — without reworking data already saved.

## Slide 3
SCHEMA — CHART 1 OF 2
Radar Model Composition — Model, Operating Mode & Waveforms
ClaweRadarInstance
Name (unique)
Description
AlternateName[] (NATO/ELNOT)
ClaweRadarModeInstance
Name (unique in radar)
RadarModeType {Search,TAR,TTR,Missile}
OperatingMode {Manual,Auto,Cognitive}
ClaweWaveformInstance
WaveformID (unique in mode)
BaseWaveform {PD, SP}
CenterFreqType {Fixed,Random}
0..N
0..N
OperatingMode «oneof»
Manual — no payload
Auto — repeating waveform Schedule
Cognitive — OptimizationType {Learning,Speed}
ClaweConstraintEnvelope
CFConstraintType {Range, Discretes} · MaxDutyCycle_percent · CPIDurationType {Fixed, Variable}
PDConstraints (0..1) and SPConstraints (0..1) — both may be set at once
ModifierStack (9, each independently toggleable) «oneof per modifier»
Phase · Frequency · PulseCompression · PRI · PW · Amplitude · LeadingEdge · TrailingEdge · Discrimination
Every branch is None-or-one-detail (e.g. LeadingEdgeModifier → None | Rampup | Prepulse)
«oneof» marks a discriminated union — exactly one branch is valid at a time, gated by a sibling enum.

## Slide 4
SCHEMA — CHART 2 OF 2
Proposed SQLite Tables — Thin Index + Canonical Blob
ClaweRadar
long: ClaweRadarPk PK
string: Name (unique, sole external handle)
string: Description
int: ModeCount (cached)
ClaweRadarAlternateName
long: ClaweRadarAlternateNamePk PK
long: ClaweRadarPk FK
enum: Type {Nato, Elnot}
string: Value
ClaweRadarProtoBlob
long: ClaweRadarPk PK, FK (shared)
bytes: ProtoBytes (full radar, serialized)
string: ProtoVersion
enum: Compression
bytes: Sha256
ClaweRadarMode
long: ClaweRadarModePk PK
long: ClaweRadarPk FK
string: Name (unique in radar)
enum: RadarModeType
enum: OperatingMode
enum: OptimizationType (nullable, Cognitive only)
ClaweRadarModeWaveform
long: ClaweRadarModeWaveformPk PK
long: ClaweRadarModePk FK
long: WaveformId (unique in mode)
string: Name
enum: BaseWaveform
1 : 0..N
1 : 1
1 : 0..N
1 : 0..N

## Slide 5
FIELD REFERENCE 1 OF 4
ClaweRadarInstance
Field | Type | Card. | Description
Name | string | 1 | Unique within the radar database. Sole external identity handle.
Description | string | 0..1 | Free-text description.
AlternateName | message | 0..N | NATO or ELNOT designator; UI should mirror STS's existing alt-name fields.
Modes | ClaweRadarModeInstance | 0..N | Radar modes belonging to this radar.

## Slide 6
FIELD REFERENCE 2 OF 4
ClaweRadarModeInstance
Field | Type | Card. | Description
Name | string | 1 | Unique within the parent radar.
RadarModeType | enum | 1 | {Search, TAR, TTR, Missile} — only TTR is initially supported.
OperatingMode | enum | 1 | {Manual, Auto, Cognitive}. Manual = operator-in-the-loop.
Auto.Schedule | WaveformID + Duration_s | 0..N | Repeating waveform schedule; Duration_s=0 plays once.
Cognitive.OptimizationType | enum | 1 if Cognitive | {Learning, Speed}.
CFConstraintType | enum | 1 | {Range, Discretes}; Range optionally Channelized.
MaxDutyCycle_percent | double | 1 | Radar blanks to comply if exceeded.
CPIDurationType | enum | 1 | {Fixed, Variable}.
PDConstraints | message | 0..1 | PRI/PW ranges + AllowedModifiers. May coexist with SPConstraints.
SPConstraints | message | 0..1 | PW range + AllowedModifiers. May coexist with PDConstraints.
Waveforms | ClaweWaveformInstance | 0..N | Waveform instances authored under this mode.

## Slide 7
FIELD REFERENCE 3 OF 4
ClaweWaveformInstance
Field | Type | Card. | Description
WaveformID | uint32 | 1 | Unique within the parent mode.
Name | string | 1 | Unique within the parent mode.
RangeResolution_s | double | 0..1 | Optional; default used if missing (typ. 100–400 ns).
CenterFreqType | enum | 1 | {Fixed, Random}; Random has optional ClearChan bool.
WaveformCompression | message | 1 | Fixed 30 dB / 1024-pt FFT for now.
BaseWaveform | enum | 1 | {PD, SP}; determines which PD-only/SP-only fields apply.
PRIType / PWType | enum | 1, PD only | Fixed, or Random/DutyCycle.
RDIIntegration | enum | 1, PD only | {None,2,4,8,16,32,64}; improves SNR vs. range/velocity res.

## Slide 8
FIELD REFERENCE 4 OF 4
Modifier Stack — All Nine, Independently Toggleable
Modifier | Branches | Applies to | Key parameters
Phase | None, PhaseEncoded | PD + SP | Reserved placeholder field, no functional params yet.
Frequency | None, SpreadSpectrum | PD + SP | ChannelSpread/SubchannelSpread; SpreadBW1/2 (10–50 MHz); SidelobeDetection.
PulseCompression | None, PSK16, Barker13, LFM | PD + SP | LFM: LFMBandwidth_hz.
PRI | None, BaseAgile, RandomAgile | PD only | DropRate% 25–75; Agility% 0–75.
PW | None, RandomAgile | PD only | Agility% 0–50.
Amplitude | None, Chop | SP only | DutyCycle% 25–75; MaxOnTime_s; IncreaseDC-before-target bool.
LeadingEdge | None, Rampup, Prepulse | PD + SP | Rampup 0.25–2 µs. Prepulse: PW/Gap/FreqType/FreqOffset/ApplyFreqMods.
TrailingEdge | None, Postpulse | PD only | Postpulse: PW/Gap/FreqType/FreqOffset/ApplyFreqMods.
Discrimination | None, LeadingEdgeTrack, WBLFM | PD + SP | WBLFM: BW 0–2 GHz, Repeat 1–4. LeadingEdgeTrack: reserved placeholder.